# Technical Challenge: Autonomous Robot Logging with ROS
## Overview
## Your task is to design and implement an experiment using ROS 2 where a simulated mobile robot autonomously navigates an environment and records key operational data. This data must be visualized, and selected events must also be recorded on a blockchain.
## Objectives
ROS Functionality
- Use ROS 2 with Gazebo to simulate a mobile robot.
- Implement autonomous navigation using a pre-defined map.
- Record robot state data including:
  - Timestamps
  - Position coordinates (x, y)
  - Status messages
Experimental Design and Data Handling
- Define a clear goal for the mobile robot. Please note that defining a single clear goal from the examples is sufficient. For example:
  - Autonomously navigating three waypoints
  - Completing an autonomous navigation loop around and indoor area
  - Avoid obstacles and arrive at destination
- Record relevant data during the experiment.
- Use a clear methodology to describe the experiment and the expected behavior.
Visualization
Plot figures that will elaborate on robot behavior and can confirm that the goal has been executed.
Blockchain
- Install and run Ganache to simulate a local Ethereum blockchain.
- Write a simple Python script using web3.py to send transactions to Ganache.
- Each time the robot executes the defined goal, submit a transaction that includes:
  - A timestamp
  - The robot’s position
  - A brief status message (e.g. “Reached waypoint 2”)
- Store this data in a smart contract or send it as a transaction payload.
## Evaluation Criteria
The resultant code will be uploaded to a public GitHub repository. Together with the code a brief description of the experiment should be included. The evaluation criteria of this technical challenge will consider the following topics:
- ROS navigation and system architecture
- Experiment design and reproducibility
- Logging, data collection and visualization
- Blockchain setup and web3 integration
- Possible improvements for future work